## Slide 1: DAQ state machine
M. de Jong

## Slide 2: Introduction (1/3)
There is one unique master
  e.g. central GUI
There is a variety of clients¶
  each client implements same state machine (next slide)
  each client communicates with master via (central) server
  each client reports messages to (central) logger
¶ This refers to shore station part of DAQ system.

## Slide 3: Introduction (2/3)
Paused
Running
Ready
Idle
Standby
ev_pause
ev_continue
ev_reset
ev_init
ev_quit
ev_configure
ev_start
ev_stop
on
ev_off
Error
ev_recover
ev_error
ev_off
Operational
RunControl

## Slide 4: Introduction (3/3)
Protocol for handshaking of state transitions is based on combination of 1) state machine logic, 2) tagged messages and 3) process name
  event names are unique by construction
  tagged messages are unambiguous by implementation
  process names are unique by implementation

## Slide 5: JLigier (1/2)
JLigier is server for inter-process communications
  protocol based on “tagged” messages
    messages can contain any data
  subscription mechanisms
    “any” receive as much data as possible with given tag
    “all” receive all data with given tag
  registration of nick name of process
    JControlHost::MyId(<nick name>);
    JLigier broadcasts message “<nick name>” with tag “Born”
    JLigier broadcasts message “<nick name>” with tag “Died” when process disconnects from JLigier (e.g. terminates)
struct JPrefix
{
char tag[TAGSIZE ¶];
long long int size;
}
¶ TAGSIZE = 8;

## Slide 6: JLigier (2/2)
point-to-point connections based on TCP/IP
  no message will be lost
    but not specified when message will arrive
order of messages maintained
  internal buffers work as FIFOs
any error is printed to terminal

## Slide 7: Implementation (1/5)
Every event has a corresponding action method
  ev_XXX  actionXXX(int length, const char* buffer)
    length = number of bytes in buffer
    buffer = input data to action
  enter  actionEnter()
  ev_off  actionExit()
void run()
{
while (active()) {
update();
}
}

## Slide 8: Implementation (2/5)
void update()
{
JPrefix prefix; server->WaitHead(prefix); const int length = prefix.getSize(); char* buffer = new char[length];
server->GetFullData(buffer, length);
update(prefix.getTag(), length, buffer); delete [] buffer;
}

## Slide 9: Implementation (3/5)
message content
  <event name>[:<event number>]#[data]
    optional data are treated as array of bytes
    data are transferred as-is to corresponding action method
event table
  map pair of (<tag>, <event name>) to CHSM event
  list of accepted tags (included by default)
    general tag “RC_CMD”
    unique tag “<IP sub-address¶>/<client name§>”
¶ IP sub-address written in hexadecimal code.
§ client name is specified on command line of application option –u <client name>

## Slide 10: Implementation (4/5)
JDAQClient::update(tag, length, buffer)
  parse event name and optional number
  look up CHSM event from event table
  trigger event
    call corresponding action method
  enter state
    send reply

## Slide 11: Implementation (5/5)
upon entering state after successful completion of state transition
  reply message is sent to JLigier
    tag “RC_REPLY”
    data “<full name>#<event name>:<event number¶>#<state name§>” where <full name> = “DAQ#<IP address†>#<client name>”
¶ From previous request for state transition.
§ complete state name is (for backward compatibility) “Main.RunControl.<state name>.” † IP address written in hexadecimal code.

## Slide 12: Special actions (1/1)
virtual void JDAQClient::setSelect(JFileDescriptorMask& mask) const;
  can be used to listen to other file descriptors (e.g. sockets)
  called before method update()
virtual void JDAQClient:: actionSelect(const JFileDescriptorMask& mask);
  can be used to implement actions for other file descriptors
  called after method update()

## Slide 13: Error handling (1/4)
State machine is either in cluster Operational or state Error
  event ev_error can be triggered any time
    exit cluster Operational
    enter state Error
  state Error can only be exited by following events
    ev_recover  enter state Operational.Idle (i.e. no history¶)
    ev_off  terminates application
¶ It is possible to specify history in CHSM.

## Slide 14: Error handling (2/4)
Exceptions in any actionXXX() method will be caught and trigger event ev_error
Upon entering state Error, standard reply message is sent, i.e:
    tag “RC_REPLY”
    data “<full name>#ev_error#Main.RunControl.Error”
Tags to trigger events ev_recover or ev_off
    general tag “RC_CMD”
    unique tag “<IPsub-address>/<clientname>”
Default implementation of corresponding action methods are empty
    virtual void actionError() {}
    virtual void actionRecover(int, const char*) {}

## Slide 15: Error handling (3/4)
Following a request for a state transition, either of the following cases will happen:
  success
    tag “RC_REPLY”
    data “<full name>#<event name>:<event number>#<state name>”
  invalid
    tag “RC_FAIL”
    data “<full name>#<event name>:<event number>#<state name>”
  termination
    tag “Died”
    data “<nick name>”
  timeout

## Slide 16: Error handling (4/4)
each state machine is also in state Responder
ev_input
  set debug level, etc.
ev_check
  sends message
    tag “RC_REPLY”
    data “<full name>#ev_check:<event number>#<state name>”
Responder
ev_input, ev_check

## Slide 17: Specifications (1/2)
client
  should receive all requests for state transition from master
    subscription to tags “RC_CMD” and <unique tag> is “all”
  should have unique nick name
    nick name equals full name
  should reply after request for state transition from master within timeout
    “AcousticDataFilter may take two minutes to complete actionConfigure()”

## Slide 18: Specifications (2/2)
master
  should receive all replies from clients
    subscription to tags “RC_REPLY”, “RC_FAIL”, “Born” and “Died” should be “all”
  should maintain state of complete system
    state transitions of clients should be synchronised i.e. all clients are in targeted state before new state transition is triggered

## Slide 19: Notifications (1/2)
JLigier subscription with “any” may result in loss of messages
  client too slow to process all messages
  JLigier will not report this as error
JLigier subscription with “all” may result in congestion
  client too slow to process all messages
  JLigier will report this as error

## Slide 20: Notifications (2/2)
client
  should not need to know state of other clients
    nonetheless JDataWriter needs handling of cases in which JDataFilter is in different run
master
  polling of state is unreliable
    state of client is given in reply message following request for a state transition
  use of ev_check should be limited to exceptional cases
    e.g. restart of master