## Slide 1: CHSM state machine
M. de Jong

## Slide 2
Paused
Running
Ready
Idle
Standby
ev_pause
ev_continue
ev_reset
ev_init
ev_quit
ev_configure
ev_start
ev_stop
on
ev_off
Error
ev_recover
ev_error
ev_off
Operational
new
RunControl

## Slide 3: Specifications (1/3)
New sub-cluster Operational and new state Error are introduced
  state machine is either in sub-cluster Operational OR state Error
Event ev_error can be triggered any time
  exit sub-cluster Operational
  enter state Error
State Error can only be exited by following events
  ev_recover  enter state Operational.Idle (i.e. no history¶)
  ev_off  terminates application
¶ It is possible to specify history in CHSM.

## Slide 4: Specifications (2/3)
Exceptions in any actionXXX() method will trigger event ev_error
Upon entering state Error, usual message with tag RC_REPLY is broadcast
  DAQ#<IPaddress>#<processname>#ev_error#Main.RunControl.Error
Possible tags for control message to trigger events ev_recover or ev_off
  general tag “RC_CMD”; or
  application specific tag “DAQ#<IPaddress>#<processname>”;

## Slide 5: Specifications (3/3)
Backward compatibility:
  name of sub-cluster Operational is removed from any communications
  default implementation of additional action methods are provided, i.e:
    virtual void actionError() {}
    virtual void actionRecover(int, const char*) {}