## Slide 1: Trigger
M. de Jong
20/4/2020

## Slide 2: “All-data-to-shore”
all analogue pulses from all PMTs that pass a pre-set threshold are timestamped off-shore;
all timestamped data are sent to shore;
all data are calibrated and filtered on shore in real time using a farm of commodity PCs;
all filtered and some summary data are distributed and saved on persistent media for further analyses;

## Slide 3: Applications (1/3)
JDataFilter
  real time filtering of detector data (not this talk)
JRandomTimesliceWriter
  produce time slices with random data
JTriggerProcessor
  offline filtering of detector data
JTriggerReprocessor
  reprocess triggered data

## Slide 4: Applications (2/3)
JTriggerEfficiency
  processing of Monte Carlo data
    output of km3, KM3Sim, JSirene, …
    addition of random background
JEventTimesliceWriter
  processing of Monte Carlo data
    output of K40 simulations
    addition random background (e.g. singles rates)

## Slide 5: Applications (3/3)
JSummary
  convert real summary data to summary data suitable for simulations
    output of ARCA or ORCA detector
JTriggerMonitor
  print trigger statistics
JTrigger
  provides statistical information about the signal processing during detector simulation of JTriggerEfficiency
    possible explanation why there are no triggered events

## Slide 6: JRandomTimesliceWriter
command line options
  -a <detector file>
  -B "R1 [R2 [R3 [...]]]" // background
  -o <output file> // time slice data
  -P "%.QE=<value>; // PMT simulation pmt=<module> <address> QE=<value>; "
  -P <PMT simulation file>
wild card

## Slide 7: JTriggerProcessor
command line options
  -a <detector file>
  -f <input file> // time slice data (see below)
  -@ "<trigger parameter>=<value>; …"
  -@ "<trigger parameter file>"

## Slide 8: JTriggerEfficiency (1/2)
command line options
  -a <detector file>
  -f <Monte Carlo event file>
  -@ "<trigger parameter>=<value>; …"
  -@ "<trigger parameter file>"
  -P "%.QE=<value>; // PMT simulation
  pmt=<module> <address> QE=<value>;"
  -P <PMT simulation file>
  -S <seed>
  -O <triggeredEventsOnly>

## Slide 9: JTriggerEfficiency (2/2)
command line options
  -B "R1 [R2 [R3 [R4 ]]]" // background rates [Hz]
  -r "file=<file name>" // run-by-run simulation
  -r <run-by-run simulation file>
  N.B. singles rates from run-by-run data (option -r) prevails but multiples rates are taken from option -B

## Slide 10: JSummary
command line options
  -f <raw data file> // real data
  -a <detector file> // for simulations
  -n <number of slices>
  -o <output file>

## Slide 11: JEventTimesliceWriter
command line options
  -f <K40 event file> // coincidence data
  -o <output file> // time slice data
  -r <event rate [Hz]>
  -B "R1 [R2 [R3 [R4 ]]]" // background rates [Hz]
  -P "%.QE=<value>; // PMT simulation pmt=<module> <address> QE=<value>;"
  -P <PMT simulation file>

## Slide 12: Detector (1/1)
Data structures
  JDetector : std::vector<JModule> {};
  JModule : std::vector<JPMT> {};
  JPMT : JObjectID, JAxis3D, JCalibration {};
JModuleRouter
  O(1) access to module data
    JModule getModule(<module identifier>);
JPMTRouter
  O(1) access to PMT data
    JPMT getPMT(<PMT identifier>);
JDAQHitRouter
  O(1) access to PMT data
    JPMT getPMT(JDAQKeyHit&);

## Slide 13: Data format (1/4)
class JDAQHit
{
getPMT(); // get PMT (0, …, 30)
getT(); // get time [ns]
getToT(); // get time-over-threshold [ns]
};
class JDAQFrame // low-level data frame
{ // one per optical module
const_iterator begin();
const_iterator end();
bool empty();
int size();
const JDAQHit& operator[](int);
};
mimics std::vector<>

## Slide 14: Data format (2/4)
class JDAQSuperFrame : // high-level data frame
// one per optical module
..
JDAQSuperFrameHeader, // run number, etc.
JDAQFrame // PMT data
{};
class JDAQTimeslice : // all data there are
..
JDAQTimesliceHeader, // run number, etc.
vector<JDAQSuperFrame> // PMT data
{};

## Slide 15: Data format (3/4)
class JDAQSummaryFrame : // summary information
.. // one per optical module
JDAQModuleIdentifier,
JDAQFrameStatus
{
bool testDAQStatus(); // UDP packet test
bool testWhiteRabbitStatus(); // White Rabbit test
bool testHighRateVeto(); // high-rate veto (do this first)
bool testHighRateVeto(int tdc); // high-rate veto
double getRate(int tdc); // rate [Hz]
};

## Slide 16: Data format (4/4)
class JDAQSummaryslice : // all summary information .. // there is
JDAQSummarysliceHeader,
vector<JDAQSummaryFrame>
{
JDAQSummaryslice( JDAQTimeslice); // build summaries
};

## Slide 17: Data processing (1/6)
global methods
  double getTime( t [ns], JCalibration) {}
  double putTime( t [ns], JCalibration) {}
auxiliary methods
  double getTime(JDAQHit, JCalibration) {}
sign convention

## Slide 18: Data processing (2/6)
JDAQFrame
  contains all data from one optical module within pre-set time window (= frame time)
  ;
specification

## Slide 19: Data processing (3/6)
first step
  convert 1-dimensional mixed array of DAQ hits to collection of time calibrated and time sorted 1-dimensional arrays per PMT
additional steps
  merge collection of 1-dimensional arrays to single time sorted 1-dimensional array
  apply coincidence logic

## Slide 20: Data processing (4/6)
first step (2)
class JSuperFrame2D :
JModuleHeader,
vector<JFrame> // time calibrated data
{
JSuperFrame1D& operator()( JDAQSuperFrame&,
JModule&);
static JSuperFrame2D<> demultiplex; // Demultiplexer
};
I/O operator

## Slide 21: Data processing (5/6)
additional steps (2)
class JSuperFrame1D :
JModuleHeader,
vector<JElement_t> // time calibrated data
{
JSuperFrame1D& operator()( JSuperFrame2D&);
static JSuperFrame1D<> multiplex; // Multiplexer
};
I/O operator

## Slide 22: Data processing (6/6)
additional steps (2)
  JBuildL0<>
    convert raw data to JHitL0 data
      JHitL0 : JDAQPMTIdentifier, JAxis3D, JHit {};
  JBuildL1<>
    convert raw data to compressed L1 data
    convert raw data to JHitL1 data
      JHitL1 : vector<JHitL0> {};
  JBuildL2<>
    select subset of L1 data
      multiplicity of L1
      maximal angle between PMT axes

## Slide 23: Hit clustering (1/2)
clusterize(.., JMatch&)
  count number of friends;
  remove element with least number of friends;
  stop when least number of friends = number of elements;
reverse_clusterize(.., JMatch&)
  count number of friends;
  keep element with most number of friends;
  stop when most number of friends = number of elements;
clusteriseWeight(.., JMatch&)
  idem using weight of elements

## Slide 24: Hit clustering (2/2)
JMatch3D
  simple causality
JMatch3G
  causality for shower with distance dependent time window (improvement due to J. Hofestädt)
JMatch3B
  causality for muon with distance dependent time window (improvement due to B. Bakker)
JMatch1D
  causality for muon along z-axis

## Slide 25: Accidental coincidence rate (1/2)
Total rate
Probability
minimum cluster size
number of sources
rate of each source

## Slide 26: Accidental coincidence rate (2/2)
3D
1D

## Slide 27: Trigger logic (1/1)
Level 1
  JBuildL1 local coincidences (Dt)
Level 2
  JBuildL2 local coincidences (Dt; cos(q); M ≥ 2)
Level 3
  trigger3DMuon
  trigger3DShower
  …
Merge events
  overlap in time
    JDAQEvent::getOverlays()
multiple trigger algorithms can be applied to the same data

## Slide 28: JTriggerEfficiency
initialisation
  detector geometry and calibration
  setup detector simulation
event loop
  input Monte Carlo event
  add background
  create JDAQTimeslice
  calibrate data
  application of trigger(s)
  output JDAQEvent
  output JDAQSummaryslice
termination
  close files
same as JDataFilter and JTriggerProcessor
handled via interfaces,
see next slides

## Slide 29: Interfaces
JK40Simulator
  generation of random background
    virtual void generateHits(JModule, JTimeRange, JModuleData& output);
    JModuleData : vector< JPMTData<JPMTSignal> > {};
JPMTSimulator
  simulation of PMT
    virtual void processHits( JPMTIdentifier, JCalibration, JStatus,
    JPMTData<JPMTSignal>& input,
    JPMTData<JPMTPulse>& output);
JCLBSimulator
  Simulation of CLB
    typedef vector< JPMTData<JPMTPulse> > JCLBInput;
    virtual void processData(JModuleIdentifier, JCLBInput input, JDAQSuperFrame& output);

## Slide 30: JK40DefaultSimulatorInterface
implements
  JK40Simulator
interface methods
  virtual double getSinglesRate(JPMTIdentifier);
  virtual double getCoincidenceRate(JModuleIdentifier, multiplicity);
  virtual double getProbability(cos(q));

## Slide 31: JPMTDefaultSimulatorInterface
implements
  JPMTSimulator
interface methods
  virtual bool getPMTstatus(JPMTIdentifier, JTimeRange, // time dependence
  JStatus); // on/off
  virtual JPMTSignalProcessorInterface // see next slide getPMTSignalProcessor(JPMTIdentifier);

## Slide 32: JPMTSignalProcessorInterface
interface methods
  virtual bool applyQE(); virtual double getRandomTime(double t_ns);
  virtual bool compare(JPhotoElectron, JPhotoElectron);
  virtual double getRandomCharge(int NPE);
  virtual JChargeDomains applyThreshold(double npe);
  virtual double getTimeOverThreshold(double npe);
  virtual double getSurvivalProbability(int NPE);
  virtual void merge(JPMTData<JPMTHit>&);

## Slide 33: JCLBDefaultSimulatorInterface
implements
  JCLBSimulator
interface methods
  virtual JDAQHit JTDC::makeHit(JPMT_t, double, JTOT_t); // non-linearity
  virtual bool JStateMachine::maybeSwapped(JDAQHit, JDAQHit); // state machine
  virtual int getUDPNumberOfReceivedPackets(JModuleIdentifier); virtual int getUDPMaximalSequenceNumber(const JModuleIdentifier); virtual bool hasUDPTrailer(const JModuleIdentifier); virtual bool getHighRateVeto(JPMTIdentifier); // high-rate veto

## Slide 34: Available implementations (1/3)
JK40DefaultSimulator
  single rates
  multiple rates
  angular dependence of coincidence rates
JPMTAnalogueSignalProcessor
  transition time spread
  gain spread
  threshold
  time-over-threshold
  hit merging

## Slide 35: Available implementations (2/3)
JCLBDefaultSimulator
  TDC non-lenarity
  hit re-shuffling

## Slide 36: Available implementations (3/3)
JK40RunByRunSimulator :
  JK40DefaultSimulator
    single rates from real data
    multiple rates
    angular dependence of coincidence rates
JPMTRunByRunSimulator :
  JPMTDefaultSimulator
    PMT status from real data
JCLBRunByRunSimulator :
  JCLBDefaultSimulator
    high-rate veto from real data

## Slide 37: Detector simulation
JDetectorSimulator :
JPMTRouter, // fast access to PMT data
JK40Simulator,
JPMTSimulator,
JCLBSimulator
{
JDetectorSimulator(JDetector); // input detector
protected:
std::auto_ptr<JK40Simulator> k40Simulator;
std::auto_ptr<JPMTSimulator> pmtSimulator;
std::auto_ptr<JCLBSimulator> clbSimulator;
};
set your favourite simulator

## Slide 38: PMT simulation (1/1)
JMonitorK40
  -f <input file> // JDAQTimeslice
  -o <output file> // histograms
JFitK40
  -f <input file> // histograms
  -P <PMT efficiency file> //
PMT efficiency file can be input to JTriggerEfficiency, JEventTimeslice, JRandomTimesliceWriter

## Slide 39: Muon depth dependence (1/1)
Depth [km]
Rate [Hz]
2.8
2.9
3.0
3.1
3.2
3.3
3.4
0.05
0.04
0.03
0.02
0.01
0.0
data
fit
KM3NeT

## Slide 40: Muon depth dependence (1/1)
data (corrected)
fit
Rate [Hz]
0.05
0.04
0.03
0.02
0.01
0.0
Depth [km]
2.8
2.9
3.0
3.1
3.2
3.3
3.4
KM3NeT

## Slide 41: Time slice (1/1)
class JEventTimeslice :
JDAQTimeslice // as raw data (!)
{
JEventTimeslice( JDAQChronometer, // RUN number, etc.
JDetectorSimulator, // detector simulation
Event, // Monte Carlo event
[JTimeRange]); // time window
};

## Slide 42: Event (1/6)
JDAQEvent :
JDAQChronometer,
JDAQTriggerCounter, // real data: unique per thread
// Monte Carlo: index to TTree
JDAQTriggerMask // trigger bits of event
{
const_iterator<..> begin<..>();
const_iterator<..> end<..>();
unsigned int size<..>();
unsigned int getOverlays();
protected:
std::vector<JDAQTriggeredHit> triggeredHits;
std::vector<JDAQSnapshotHit> snapshotHits;
};
<..> select data type

## Slide 43: Event (2/6)
JDAQTriggerMask {}; // 64 bit coded word, 1 bit per trigger // macro setTriggerBit(<trigger>, <bit>);
JDAQKeyHit :
JDAQModuleIdentifier, // module JDAQHit // PMT hit {};
typedef JDAQKeyHit JDAQSnapshotHit; // snap shot hit
JDAQTriggeredHit : // triggered hit
JDAQKeyHit, // same as snapshot hit JDAQTriggerMask // trigger bits of hit
{};

## Slide 44: Event (3/6)
{JDAQTriggeredHit}
time
Tmin
Tmax
trigger(s)
Tmax + DT
Tmin - DT
snapshot
{ hit }
¶ DT = nD/c (where D corresponds to size of detector)
,JDAQSnapshotHit}
{JDAQSnapshotHit,
snapshot¶ = All raw data between [Tmin - DT, Tmax + DT]

## Slide 45: Event (4/6)
{JDAQTriggeredHit}
Tmin
Tmax
{JDAQTriggeredHit}
Tmin
Tmax
{JDAQTriggeredHit}
JDAQEvent :
..
JDAQTriggerMask // ORed
{
unsigned int getOverlays(); // incremented
};
JDAQTriggeredHit :
.. JDAQTriggerMask // ORed
{}

## Slide 46: Event (5/6)
class JTriggeredEvent :
JDAQEvent // I/O
{
JTriggeredEvent( JEvent, // internal to trigger
JTimesliceRouter, // see next slide
TMaxLocal_ns, // L1 time window
[snapshot]); // option
};

## Slide 47: Event (6/6)
class JTimesliceRouter :
JPointer<const JDAQTimeslice> // pointer to raw data
{
configure(JDAQTimeslice); // input
JDAQFrameSubset getFrameSubset( JDAQModuleIdentifier, JTimeRange);
};
subset of JDAQSuperFrame

## Slide 48: Examples (1/4)
JSignalL1 & JRandomL1
  test efficiency and purity of L1L2 coincidence logic
JFilter
  test efficiency and purity of cluster methods
JVolume1D
  plot trigger effective volume

## Slide 49: Examples (2/4)
number of hits
efficiency
JRandomL1.sh
JSignalL1.sh
number of hits
efficiency

## Slide 50: Examples (3/4)
number of hits
number of hits
JFilter.sh
efficiency
purity

## Slide 51: Examples (4/4)
En [GeV]
Volume [km3]
JVolume1D.sh