## Slide 1: JTuneHV Revision
2020-01-07

## Slide 2: Summary
Plotting removed from JTuneHV.sh
Several modifications of JTuneHV.cc:
  JTuneHV no longer looks up vendor high-voltages for failures
  Sets result for failed evaluations to zero
  Inter-/extrapolation moved entirely to `interpolator` data structure
Three new applications:
  JPrintTuneHV.cc
    For printing JSON output of JTuneHV
    Can be used to write out all entries with the FAILED label (other than dead modules) to a separate JSON file
  JEditTuneHV.cc
    For treating all entries labeled FAILED within a given JSON file
    Three options:
      Vendor
      run HV-settings,
      manual specifications
  JMergeTuneHV.cc
    For merging two or more JSON output files into one

## Slide 3: JTuneHV
A bash script called JTuneHV.sh, incorporating the full analysis chain, can be found in software/JCalibrate
  Main output: JSON file (to be uploaded to the database) + ROOT file (with HV-gain diagrams)
Raw data files
of the
calibration runs
Detector file corresponding to the calibration runs
PMT parameters file
Output
directory
HV-tuning analysis chain consists of three steps:
  Generating ToT-distributions for all calibration runs, using single photo-electron hits (JCalibrateToT)
  Fitting the gains for each calibration run (JFitToT)
  Matching the gain-estimates with the corresponding high-voltages for each run and performing a linear interpolation of the high-voltage corresponing to a gain of 1.0 on log-log scale

## Slide 4: JPrintTuneHV
Loops over all HV-calibrations within a given JSON file and prints all corresponding data entries
The option –o ${OUTPUTFILE} can be used to write all failures (other than dead modules) to a separate JSON file for further evaluation/treatment

## Slide 5: JEditTuneHV
Collects all HV-calibrations within a given JSON file with the FAILED status label and adjusts the `supply-voltage` field according to either:
  The high-voltage settings corresponding to a specific DAQ run, if both detector ID and run number are specified
  The vendor high-voltage settings if the detector ID is specified, but the run number is left unspecified
  Manually specifiable values if both detector ID and run number are left unspecified
The option –o ${OUTPUTFILE} can be used to write all failures (other than dead modules) to a separate JSON file for further evaluation/treatment
If successful, update status label to OK

## Slide 6: JMergeTuneHV
Takes two or more HV-calibration JSON files and merges them into one
N.B.: if a PMT appears in multiple files, only the calibration of the first specified file is kept